|  | OFFICE OF SPECIAL EVENTS 200 South Lamar, Austin, Texas 78704 (512)974-6797 (512) 974-6756 Fax reservations@austintexas.gov http://www.austintexas.gov/parkevents |
| --- | --- |

Approved Ground Protection Materials Per the

Access/Use Guidelines and Policy for Events

Protecting and Preserving Turf / Tree Areas

The following items are key expectations of all users of irrigated parkland turf areas, and trees.  They are organized by area, and then expected performance and/or guidelines.

Approved

Ground Cover Materials

(Approved)   Terraplas

Ideal for:  Vendor areas, bars, pathways for dollied materials, roadway for light duty (carts only).

NOT for:  forklifts, box trucks, loaders, or similar/larger.

- Superior light and air penetration. 	Superb grounds protection from rain.

- Superior for use under vendors.

(Approved)   MegaDeck

Ideal for:  Heavy weight bearing areas.  Forklifts, box trucks, loaders, or similar.

| Extreme Compressive Load Capabilities (up to 600psi) | MegaDeck can support heavy static and rolling loads, including staging, light towers, cranes, buses and bleachers. |
| --- | --- |
| Metal Cam Lock Connection System | MegaDeck rig mats lock firmly together without allowing any shifting or slop at connection points as the cam lock receiver maintains its integrity. |
| 7.5' x 14' Mat Dimensions | MegaDeck is properly sized to lay flat in standard ISO containers, simplifying handling, packaging & equipment needs while reducing upfront expenses. |
| Unique Manufacturing Process | MegaDeck is stronger than other plastic matting systems that contain voids due to incomplete melting during the molding process. |
| Proprietary HDPE Composite Formula | MegaDeck's unique blend of virgin HDPE, proprietary fillers, UV protection, anti-static and other additives is non-absorbent and prevents sparking, degradation, expansion and related bowing due to temperature variances, while strengthening the plastic. |
| Overlapping Flanges | MegaDeck's overlapping flanges ease installation and add strength along connection seams. |

(Approved)   LD Panels

Ideal for:  Vendor areas, bars, pathways for dollied materials, roadway for light duty (carts only), forklifts, box trucks, loaders, or similar.

Requires product to be lifted/reinstalled to not smother grounds.

- Limit the amount of time the decking is on the ground to no more than 24 hours with a substantial break period between applications.   Turf areas must breathe.  Decking put down on one day of load in should be picked up overnight and reinstalled for additional second day load in activities.

(Approved)   Bill Jax or Decking Platforms

Ideal for:  Vendor areas, bars, pathways for dollied materials, roadway for light duty (carts only).

NOT for:  forklifts, box trucks, loaders, or similar.

- Superior light and air penetration.

- Superb grounds protection from rain.

- Superior for use under vendors.

(Approved – with restrictions)  DuraDeck

Ideal for:  limited period use pathways (single day) for light weight bearing requirements.

NOT for:  semis, forklifts, box trucks, loaders, or similar.

- Inferior light and air penetration.

- Limited grounds protection from rain.

- Limited for use under vendors – no ventilation or drainage.

Dark tinted product will have increase heat retention and radiation, and thus is susceptable to smother/scorch the ground underneath.

NON Approved

Ground Cover Materials

(NOT Approved)   Hexagon ground cover

Issues

No mechanism for turf to breath.

Easily heats to unacceptable levels, quickly killing turf.

Product has been slippery from experience with mild/moderate moisture.

MAY work to cover completely bare ground spaces in finite areas.

(NOT Approved)   Plywood ground cover

Issues

Wood decking, plywood or similar employed during the load in/out provides some protection in extremely limited scenarios, however is ultimately insufficient to the task of effectively distribution weight/loads across the surface.

The product typically succumbs to weight and cracks/splits, further negating any weight distribution properties.

No mechanism for turf to breath.

Warps easily with moderate moistuire.

Decking/surfaces Required for Multi-Day Events Under Food Vendors:

General concession areas at any multi-day event shall install raised decking general work areas surfaces under front of house vending areas.  For example, a 2-4” raised 20x20 deck under each vendor front of house for general work areas, and where approved, back of house mats/surfaces which are manually picked up nightly.

Where approved by PARD, floor mats, tables, and similar back of house items should be set up at the last minute possible to limit the amount of time those mats are on the ground killing turf areas.  Likewise, they should be picked up nightly after the concession area is cleaned of litter.

Garden carts and hand pulled flat beds are ideal for vendor general product load in.

Devices that hold/contain water/grey water should sit on a riser which allows air movement under the device.  Where water must be removed from them daily, it may NOT be done on turf, and should be bucket/carried/flex piped out of the area.

DuraBase, LD Panels or similar is superb in most respects.  This decking material is entirely sufficient to the task, and organizers must strive to have something that substantial under any truck, crane, semi full of ice, or heavily laden forklift that needs to drive on the turf.